## Slide 1: A Maximum Likelihood Approach to Extract Polylines from 2-D Laser Range Scans
Alexander Schaefer, Daniel Büscher, Lukas Luft, Wolfram Burgard

## Slide 2: Motivation for line extraction
Man-made environments often consist of linear structures
We propose a probabilistic method to extract polylines from 2-D laser range scans
Key idea: maximize the meas. likelihood of a given scan with as few lines as possible
  Two-step Probabilistic Line Extraction (PLE) algorithm:
    Polyline Extraction
    Polyline Optimization

## Slide 3: 1. Polyline extraction
Start by connecting all neighboring scan endpoints
Very distant endpoints are not connected ( parameter)
Iteratively remove vertex j* such that the least error in meas. probability is induced
Also remove lines with few endpoints (set )
Stopping criteria: number of lines, error (increment), …
Notes: First step: definition of the polyline topologies

## Slide 4: 2. Polyline Optimization
Second step: optimize polyline vertex positions
Up to now, vertices positioned on ray endpoints (suboptimal)
Apply numerical optimization to further reduce meas. error
Endpoints of polylines allowed to move on the ray
Intermediate points move freely

## Slide 5: Results
Our PLE significantly outperforms other common algorithms
Evaluated on real and sim. data (RMSE, fraction reflected rays, …)
More details at the poster
Split-and-Merge
(SAM)
PLE